## Slide 1: Tutorials for STM32F103RB
Nicolas Barbot, Edouard BURTZ
2017

## Slide 2: Tutorials for STM32F103RB
Create an OpenSTM32 Project
Create a STM32CubeMX Project
GPIO
UART
Timer
Analog to Digital Conversion
Digital to Analog Conversion
FLASH

## Slide 3: Tutorials for STM32F103RB
Ressources
  Nucleo F103RB
    http://www.st.com/content/st_com/en/products/evaluation-tools/product-evaluation-tools/mcu-eval-tools/stm32-mcu-eval-tools/stm32-mcu-nucleo/nucleo-f103rb.html
    This page contains user manual UM1724 describing the hardware of Nucleo boards
  STM32F103RB
    http://www.st.com/content/st_com/en/products/microcontrollers/stm32-32-bit-arm-cortex-mcus/stm32f1-series/stm32f103/stm32f103rb.html
    This page contains reference manual RM0008 describing STM32F103RB
  STM32 Cube F1
    http://www.st.com/content/st_com/en/products/embedded-software/mcus-embedded-software/stm32-embedded-software/stm32cube-embedded-software/stm32cubef1.html
    This page contains UM1850 describing the HAL library
  Open STM32
    http://www.openstm32.org/HomePage
    Open STM32 is a free Eclipse plugin for programming STM32 MCU (registration needed).
  Eclipse
    https://www.eclipse.org
    Eclipse is the IDE software
  Hardware Shield
    ###### TBD ######
    This page describe the shield hardware for Nucleo board (Arduino connector)

## Slide 4: Using ADC

## Slide 5: Using ADC
Goals:
  Identify adc from the datasheet
  Configure and use timers with the ADC library
  Use the ADC to verify an analogic level and trigg an alarm
Requirement
  Create an OpenSTM32 Project
  GPIO

## Slide 6: Identify ADC
Open Reference Manuel RM0008 [2]
  This document describes the STMF103RB.
  Two 12 bits Analog to Digital Converter (ADC1 & ADC2)
  16 external channels for each ADC
  Conversion in single shot or scan mode, possibility of DMA
In this tutorial, we will configure the ADC1 in mode Single continuous (simplest mode) to acquire voltage value.

## Slide 7: Create the Project
Create a new project for STM32F103RB using HAL library
  See “CreateOpenSTM32Project” presentation
Add the SystemClock_Config function in main.c
  Set HCLK to 64 MHz
Call SystemClock_Config and HAL_Init function in main().

## Slide 8: Using ADC
Open Hardware shield schématic document [4]
  This document describes the hardware layout of shield connected on arduino connector of the Nucleo boards.
This shield provide different hardware input and output
  Two adjustable resistors “POT1” and “POT2” which provides 2 analog voltages between 0 and 3,3V
  A bicolour Led (Red and orange) “LED1” and “LED2”
Configure the GPIO:
  Configure the GPIO output for driving the bicolour Led
  Configure the GPIO Input for acquire an analogic voltage on “POT1” (GPIO_MODE_ANALOG, GPIO_NOPULL, GPIO_SPEED_FREQ_HIGH)
  Make sure that the choosen GPIO_Pin correspond to the STM32 port pin (User Manuel 1724 « STM32 Nucleo-64 boards, page 39)

## Slide 9: Using ADC
Open User Manuel 1850 « Description of STM32F1xx HAL drivers » [3]
  Chapter 4 (p. 82) describes the use of ADC
  ADC must be configured at RCC top level. In HAL_ADC_MspInit declare a RCC_PeriphCLKInitTypeDef variable and set the field as describe in [doc3] page 85. then call HAL_RCCEx_PeriphCLKConfig() function.
  Call __HAL_RCC_ADCx_CLK_ENABLE() to enabling clock for the corresponding ADC.
  You must select the operation mode: Declare an ADC_HandleTypeDef global variable . In Main init, affect it with « data alignement right », « scan disable », « continuous mode » and « software trigg » for configuring the ADC in desired mode. Set the corresponding instance.
  Call HAL_ADC_Init()
  You must select the conversion channel and sample time: Declare an ADC_ChannelConfTypeDef variable. In Main init, affect it for selecting the corresponding channel , « ADC_REGULAR_RANK_1 » and « ADC_SAMPLETIME_41CYCLES_5 «
  Call HAL_ADC_ConfigChannel()
  Call HAL_ADC_Start()
  In the main loop call HAL_ADC_PollForConversion () to wait for end of conversion then call HAL_ADC_GetValue() for getting the converted value

## Slide 10: Using ADC
Test your software
  Put a breakpoint on the next instruction after reading the converted value. Verify the value in the result variable compared to the analogical value on the analog input. Make several test.
Manage an alarm according to voltage value on analog input
  Complete your program with the specification below. Then test it.
  Improve your software in adding an hysteresis for the red LED (see specification below). Then test it.
Vin | Orange LED | Red LED
Vin < 1V | OFF | OFF
1V ≤ Vin ≤ 2V | ON | OFF
Vin > 2V | OFF | ON
Vin | Red LED
Increase and Vin > 2V | ON
Decrease and Vin ≤ 1.5V | OFF

## Slide 11: Conclusion
Thanks to this tutorial, you are now able to:
  Configure an use ADC
  Convert analogical value for numeric treatment