## Slide 1: Tutorials for STM32F103RB
Nicolas Barbot
2016

## Slide 2: Tutorials for STM32F103RB
Create an OpenSTM32 Project
Create a STM32CubeMX Project
GPIO
UART
Timer
Analog to Digital Conversion
Digital to Analog Conversion
FLASH

## Slide 3: Tutorials for STM32F103RB
Ressources
  Nucleo F103RB
    http://www.st.com/content/st_com/en/products/evaluation-tools/product-evaluation-tools/mcu-eval-tools/stm32-mcu-eval-tools/stm32-mcu-nucleo/nucleo-f103rb.html
    This page contains user manual UM1724 describing the hardware of Nucleo boards
  STM32F103RB
    http://www.st.com/content/st_com/en/products/microcontrollers/stm32-32-bit-arm-cortex-mcus/stm32f1-series/stm32f103/stm32f103rb.html
    This page contains reference manual RM0008 describing STM32F103RB
  STM32 Cube F1
    http://www.st.com/content/st_com/en/products/embedded-software/mcus-embedded-software/stm32-embedded-software/stm32cube-embedded-software/stm32cubef1.html
    This page contains UM1850 describing the HAL library
  Open STM32
    http://www.openstm32.org/HomePage
    Open STM32 is a free Eclipse plugin for programming STM32 MCU (registration needed).
  Eclipse
    https://www.eclipse.org
    Eclipse is the IDE software

## Slide 4: Using timers

## Slide 5: Using timers
Goals:
  To identify timers from the datasheet
  To configure and use timers with the TIM library
  To set up a time base to generate a periodic interruption
Requirement
  Create an OpenSTM32 Project
  GPIO

## Slide 6: Identify timers
Open Reference Manuel RM0008 [2]
  This document describes the STMF103RB.
  General purpose timers: TIM2 to TIM5 (16 bit counter, 4 channels)
  General purpose timers: TIM9 to TIM14 (16 bit counter, 2 channels)
  Basic timers: TIM6 and TIM7 (often used to drive digital to analog converter)
  Advenced-control timers: TIM1 and TIM8 (16 bit counter, 4 channels, repetition counter)
In this tutorial, we will configure the TIM2 to generate an interruption every second.

## Slide 7: Create the Project
Create a new project for STM32F103RB using HAL library
  See “CreateOpenSTM32Project” presentation
Add the SystemClock_Config function in main.c
  Set HCLK to 64 MHz
Call SystemClock_Config and HAL_Init function in main().

## Slide 8: Using timers
Open User Manuel 1850 « Description of STM32F1xx HAL drivers » [3]
  Chapter 39 (p. 529) describes the use of TIM driver
  By default TIM2 clock is driven by APB1 clock and runs at the same speed as HCLK and SystemCoreClock (64 MHz).
  Declare a TIM_HandleTypeDef. Set Instance to TIM2 and configure the timer to count every 0.1 ms and generate an event every second.
  Add stm32f1xx_hal_msp.c to your project. This file implements HAL_TIM_Base_MspInit() function for TIM3 and is called by HAL_TIM_Base_Init()
  Call HAL_TIM_Base_Init()
  Call HAL_TIM_Base_Start_IT()
  Overload TIM2_IRQHandler() (in stm32f1xx_it.c) to call HAL_TIM_IRQHandler()
  Define HAL_TIM_PeriodElapsedCallback() to toogle LD2 every second
  Build and check that LD2 is blincking every second

## Slide 9: Conclusion
Thanks to this tutorial, you are now able to:
  Configure an use timer
  Generate a periodic interruption