## Slide 1: Tutorials for STM32F103RB
Nicolas Barbot
2016

## Slide 2: Tutorials for STM32F103RB
Create an OpenSTM32 Project
Create a STM32CubeMX Project
GPIO
UART
Timer
Analog to Digital Conversion
Digital to Analog Conversion
FLASH

## Slide 3: Tutorials for STM32F103RB
Ressources
  Nucleo F103RB
    http://www.st.com/content/st_com/en/products/evaluation-tools/product-evaluation-tools/mcu-eval-tools/stm32-mcu-eval-tools/stm32-mcu-nucleo/nucleo-f103rb.html
    This page contains user manual UM1724 describing the hardware of Nucleo boards
  STM32F103RB
    http://www.st.com/content/st_com/en/products/microcontrollers/stm32-32-bit-arm-cortex-mcus/stm32f1-series/stm32f103/stm32f103rb.html
    This page contains reference manual RM0008 describing STM32F103RB
  STM32 Cube F1
    http://www.st.com/content/st_com/en/products/embedded-software/mcus-embedded-software/stm32-embedded-software/stm32cube-embedded-software/stm32cubef1.html
    This page contains UM1850 describing the HAL library
  Open STM32
    http://www.openstm32.org/HomePage
    Open STM32 is a free Eclipse plugin for programming STM32 MCU (registration needed).
  Eclipse
    https://www.eclipse.org
    Eclipse is the IDE software

## Slide 4: Using UART

## Slide 5: Using UART
Goals:
  Identify UARTs from the datasheet
  Configure and use UART with HAL drivers (transmission and reception)
  Use printf() with UART

## Slide 6: Identify a UARTs
Open User Manuel 1724 « STM32 Nucleo-64 boards » [1]
  Go to 6.8 USART Communication (p.24), STM32F103RB provides 3 USART
  For USART1, PA9 and PA10 are connected to D8 and D2 (Arduino connectors) and CN10 pin 21 and 33 (Morpho connectors)
  For USART2, PA2 and PA3 are connected to ST-LINK by default (and then connected to USB)
  For USART3, PC10 and PC11 are connected to CN7 pin 1 and 2 (Morpho connectors)
In this tutorial, we will configure USAR2 to send and receive characters to the host PC
 | TX | RX
USART1 | PA9 | PA10
USART2 | PA2 | PA3
USART3 | PB10 | PB11

## Slide 7: Create the Project
Create a new project for STM32F103RB using HAL library
  See “CreateOpenSTM32Project” presentation
Add the SystemClock_Config function in main.c
  Set HCLK to 64 MHz
Call SystemClock_Config and HAL_Init function in main().

## Slide 8: Using UART
Open User Manuel 1850 « Description of STM32F1xx HAL drivers » [3]
  Chapter 41 (p. 598) describes the use of UART with HAL drivers (all UART, USART, SMARTCARD and IRDA driver modules control USART peripherals).
  Declare a global UART_HandleTypeDef structure (outside main())
  Fill up the structure fields to:
  Call HAL_UART_Init() function to initialize USART2
Instance | Baud rate | Word length | Stop bit | Parity | HW control | Mode
USART2 | 9600 | 8 | 1 | None | None | TX/RX

## Slide 9: Using UART
By default HAL_UART_Init() call HAL_UART_MspInit()
  HAL_UART_MspInit() is an empty function (declared in stm32f1xx_hal_uart.c file) with weak attribute and have to be overloaded to configure USART2 pins
In the project, add the file stm32f1xx_hal_msp.c
  This file contains the overloaded HAL_UART_MspInit() function for USART2
  This function enables clocks corresponding to USART2 and configure PA2 and PA3 in alternate function mode
  Implement an infinite loop in main() to transmit a character (with HAL_UART_Transmit()) every 500 ms
To see the transmitted character, open a screen session
  screen /dev/ttyACM0 9600
  Exit with Ctrl+A k and y(es)
Build the project, check that the overloaded function is executed and validate your application.

## Slide 10: Echo server
Write a program that echo each received character (from and to USART2)
  Validate your program (using screen) for simple letter
  Deal with end line
Write a program to implement Caesar cipher
  https://en.wikipedia.org/wiki/Caesar_cipher
  Plaintext is typed with the keyboard
  Ciphertext is print on the screen

## Slide 11: Using printf()
By default printf() function calls _write() which calls __io_putchar() (all functions are declared in syscalls.c file)
  _write() function is just a loop which calls __io_putchar() for every character
  __ioput_char is declared as weak and can be overloaded
In main.c, declare an new __io_putchar() function
  __io_putchar() have to transmit a single character to USART2
  In main(), call printf()
Build and validate your program

## Slide 12: Conclusion
Thanks to this tutorial, you are now able to:
  Use UART to transmit and receive characters
  Redirect printf() function to send characters to USART